## Slide 1
ALMA MATER STUDIORUM — UNIVERSITY of BOLOGNA
PMAO PROJECT · FINAL REPORT · ACADEMIC YEAR 2025/2026
A Decision Support System
for an automotive manufacturing facility
AUTHORS
Marco Buonfantino
Andrea Cevenini

## Slide 2
INTRODUCTION
The Manufacturing Environment and DSS Architecture
A flexible Factory producing six automotive families Brakes, Clutches, Pistons, Shafts, Shifts, Wheels. Each product has multi-stage cycles and complex BoM routed across distinct work centers.
P01
Brake
P02
Clutch
P03
Shift
P04
Piston
P05
Shaft
P06
Wheel
9
machine types (M01 → M21)
13
manual assembly benches
PMAO · BUONFANTINO · CEVENINI 03
DSS PIPELINE
MS Access Database
machines · suppliers · calendar etc.
↓
AMPL Models
mathematical formulation
↓
Gurobi Solver
cost-minimal, constraint and feasible decisions

## Slide 3
METHODOLOGICAL FRAMEWORK
Four decoupled layers, one coherent plan
Hierarchical Production Planning: each layer's output becomes the next layer's rigid input.
LAYER 1
RRP
Resource Requirement Planning
Annual
Sizes the machine park, hires the workforce, accepts/rejects orders to maximize profit.
LAYER 2
MPS
Master Production Schedule
12 monthly buckets
Balancing inventory holding vs. setup costs to fix monthly production volumes X[p,t].
LAYER 3
Green MRP
Material Requirements Planning
BOM explosion · CO2 Tax
Couples raw-material demand with discrete supplier batches and penalizes carbon emissions.
LAYER 4
Job Shop
Operational Scheduling
Continuous : minute level
Respects sequences of batches, allocates parallel machine copies, solves disjunctive non-overlap constraints.
PMAO · BUONFANTINO · CEVENINI 04

## Slide 4
ANNUAL CAPACITY PLANNING
Maximise profit, size the factory from scratch
DECISION VARIABLES
Accepted[p,t]
binary -> accept or reject each order
MachQuantity[m]
integer -> CNC machines to purchase
sw
integer -> seasonal workers to hire (wt = 0)
OBJECTIVE & CONSTRAINTS
max Production_Profit
Revenue - Production Cost − Machine depreciation − Labor cost (sw · wc)
Machine Capacity
monthly bucket · setup ∙ DemandProfile counted
Labor Capacity
assembly + handling + setup absorbed by wt + sw
FOCUS
SetupTime hits both constraints: machine stopped and operator engaged.
PMAO · BUONFANTINO · CEVENINI 05
RRP

## Slide 5
RRP SOLUTIONS
Optimal capacity sizing
NET PROFIT
€11,307,600
261 working days
Σ MACHQUANTITY[M]
16 units
WORKFORCE (WT + SW)
0 + 61 = 61
all seasonal hires
MACHINE COMPOSITION ACROSS RRP SCENARIOS
PMAO · BUONFANTINO · CEVENINI 06
MACHINELIMIT
Σ MachQuantity ≤ 9
REVENUEDROP
Revenue[Brake] · 0.10
WORKERLIMIT
sw ≤ 30

## Slide 6
From annual volume to monthly batches
The MPS inherits the RRP machine park and the accepted demand, then decides when and how much to launch, minimising the trade-off between inventory holding and setup costs.
DECISION VARIABLES:
X[p,t]
units completed at t
S[p,t]
end-of-period stock
RO[p,t]
production orders (batches) released at time t
SPO[p,t]
orders completed (exit) at time t
CORE CONSTRAINTS:
Inv_Balance S[t−1] + X[t] = Demand + S[t]
LeadTime_Link SPO[p,t] = RO[p, t−LTPP]
Batch Sizing MinBatchProd ≤ X ≤ MaxBatchCap
Prod_Capacity ProcTime·X + SetupTime·RO ≤ AvailCap
PMAO · BUONFANTINO · CEVENINI 08
MPS
OBJECTIVE FUNCTION
minimize Total_MPS_Cost:
UnitProdCost ·X + HoldingCostComp ·S + SetupCost · RO + BatchCost · SPO

## Slide 7
MPS SOLUTIONS
12 Months Plan
TOTAL COST
€273,711
ORDER COMPLETED
100% from RRP
BASELINE
PMAO · BUONFANTINO · CEVENINI 09
CAPACITYDROP (CAP HALVED AT T = 6)
ZEROINVENTORY
HIGHSETUP
Σ X[P,T]
43,664 units
Σ SPO[P,T]
551 batches

## Slide 8
GREEN MRP
Internalizing Carbon Costs in Supply Chain Operations
A deliberate design choice: CO2 emissions are an integral, structural part of the transportation logic. The solver minimises cost while penalising the supplier-network footprint.
OBJECTIVE FUNCTION
Min Total_MRP_Cost
Holding · Inv + (CostOfBox/PcsPerBox) · ArrivalQty + SetupOrderCost · Y
SetupOrderCost = Distance ·(CostPerKm + CO2EmissionPerKm · CO2Tax)
KEY MECHANISMS
BOM Explosion
GrossReq generated at t with LTPP offset
Rigid Packaging
RO_Comp = NumBoxes · PcsPerBox
Green Big-M Switch
NumBoxes > 0 → Y[c,s,t] = 1 (truck dispatched)
Dual-Zone Warehouse
Inbound (Inv, MagInit) Outbound (S, InitInv)
PMAO DSS · BUONFANTINO · CEVENINI 11
SUSTAINABLE MATERIAL SOURCING
Leadtime
Assumption: monthly plan Lt_Supp=0

## Slide 9
GREEN MRP
Mass-balance verification and inventory profile
TOTAL SUPPLY-CHAIN COST
€9,752,840
NUMBOXES[BRAKEBOX, S30, 1]
122 boxes
CO2PENALTY (S30)
€896.10
COMPONENT ARRIVALS VS. INVENTORY LEVEL — BASELINE (LEFT) AND HIGH STORAGE COST (RIGHT)
MASS-BALANCE at t=1 for Brakebox
MagInit (t = 0) 100 + 122 · PcsPerBox(50)= 6,200
6200 - GrossReq[BrakeBox,1] (822) = 5378
Inv[BrakeBox, 1]= 5378 units
END-OF-HORIZON
Inv[BrakeBox,t]: 1486 → 24 from t = 10 → 12. The Y[c,s,t] switch correctly drops to 0 when NumBoxes = 0 — no phantom CO2 emissions.
PMAO · BUONFANTINO · CEVENINI 14

## Slide 10
GREEN MRP STRESS TESTS
Carbon-tax procurement shift and High storage cost
AGGRESSIVE CARBON TAX: TOTAL BOXES ORDERED PER SUPPLIER IN ONE YEAR
S27 (710 km) collapses from 21,000 to 0 boxes delivered in one year that are fully reallocated to S07 (54 km), which jumps from 29k to 50k ordered boxes.
VOLUMETRIC STORAGE SURGE: TOTAL SUPPLIER DELIVERIES Y[C,S,T] IN ONE YEAR
Storage shock pushes from Y=176 (baseline) to Y=213 dispatches to keep Inv → 0.
Conversely, highCO2 consolidates loads to 138 dispatches.
PMAO· BUONFANTINO · CEVENINI 15

## Slide 11
OPERATIONAL SCHEDULING
From monthly buckets to minute-level sequencing
A continuous-time model that answers when each batch starts, which physical copy of the machine runs it and how long the entire workload takes.
DECISION VARIABLES
Makespan
universal shop-floor clock (min)
StartTime[p,i,m]
exact start minute of lot i on machine type m
Alloc[p,i,m,k]
binary — assigns lot i of product p to physical copy k of machine m
Z[p1,i1,p2,i2,m]
disjunctive sequence switch (Big-M)
WORKFORCE ARCHITECTURE
Asymmetric labour allocation
22
CNC team · 1 operator / machine
39
Assembly · 3 operators / bench
ACCELERATION TRICK
ProcTime[AssemblyTable] ÷ WorkersPerBench (3) simulates simultaneous manual throughput.
ProcTime [AssemblyTable] = ManualAssembly
SetupTime[AssemblyTable] = 0
PMAO · BUONFANTINO · CEVENINI 14
JOB SHOP SCHEDULING
Assumptions
13 pre-existing Assembly Tables in our company
Number of batches (lot) and quantity of products per batch decided on the Access Database

## Slide 12
JOB SHOP FULL WORKLOAD · MAKESPAN
Makespan = 6,312 min — workload fits inside one monthly bucket (21 working days)
MAKESPAN
6,312 min (purely experimental)
HOURS
105.2 h
8H SHIFTS
13.15 working days (conservative assumption)
WORKFORCE
22 + 39
CNC · Assembly (3/bench)
FULL GANTT: ALL 6 FAMILIES ON 16 CNC COPIES + 13 ASSEMBLYTABLE COPIES
PMAO · BUONFANTINO · CEVENINI 14

## Slide 13
CONCLUSION & SYNTHESIS
Unified Production Framework: From Strategy to Execution
RRP
€11.3M
annual profit · 16 machines · 61 workers
MPS
€273K
operational cost · 43,664 units · 100% Service Level from RRP
MRP
€9.75M
supply chain · CO₂ tax embedded
JOB SHOP
6,312min
makespan · zero overlap · fits one bucket
Hierarchical decoupling works
Each layer's output is the next layer's rigid input — strategic stability above, operational precision below, no conflicts in between.
Validated and elastic
Across nine stress-test scenarios (financial, operational, environmental) the DSS adapts without infeasibility and preserves service level.
PMAO · BUONFANTINO · CEVENINI 16

## Slide 14
THANK YOU
Questions & Discussion
PROJECT
Decision Support System for an automotive manufacturing facility
TEAM
Marco Buonfantino
Andrea Cevenini